## Slide 1: Real time System: CPU scheduling
Real-Time Systems: Real time system characteristics and kernel features, Implementing real-time operating system, real-time CPU scheduling.

## Slide 2: Overview
System Characteristics
Features of Real-Time Systems
Implementing Real-Time Operating Systems
Real-Time CPU Scheduling

## Slide 3: Introduction
A real-time system requires that results be produced within a specified deadline period
An embedded system is a computing device that is part of a larger system (I.e. automobile, airliner)
A safety-critical system is a real-time system with catastrophic results in case of failure

## Slide 4: Hard Vs Soft RTS
A hard real-time system guarantees that real- time tasks be completed within their required deadlines.
A soft real-time system provides priority of real-time tasks over non real time tasks"
Periodic and aperiodic tasks."
Starting deadline/ completion deadline."

## Slide 5: RTS Characteristic
Single purpose
Small size
Inexpensively mass-produced
Specific timing requirements

## Slide 6: RTS Characteristic
Many real-time systems are designed using system-on-a-chip (SOC) strategy.
SOC allows the CPU, memory, memory-management unit, and attached peripheral ports (i.e., USB) to be contained in a single integrated circuit.

## Slide 7: Real Time Kernels
Most real-time systems do not provide the features found in a standard desktop system
Because:
  Real-time systems are typically single-purpose
  Real-time systems often do not require interfacing with a user

## Slide 8: Implementing Real-Time Systems
In general, real-time operating systems must provide:
  Preemptive, priority-based scheduling.
  Preemptive kernels.
  Latency must be minimized

## Slide 9: Minimizing Latency
Event latency is the amount of time from when an event occurs to when it is serviced

## Slide 10: Interrupt Latency
Interrupt latency is the period of time from when an interrupt arrives at the CPU to when it is serviced

## Slide 11: Dispatch Latency
Dispatch latency is the amount of time required for the scheduler to stop one process and start another"

## Slide 12: RTS scheduling
How to schedule the Tasks such that given timing constraints are satisfied?

## Slide 13: Task models
Non periodic/Aperiodic (three parameters)
  A: arriving time
  C: computing time
  D: deadline (relative deadline)
Timing constraints: deadline for each task,
  Relative to arriving time or absolute deadline

## Slide 14: Scheduling Problem
Given a set of tasks (ready queue)
  Check if the set is schedulable
  If yes, construct a schedule to meet all deadlines
  If no, construct an optimal schedule e.g. minimizing response times

## Slide 15: Tasks with the same arrival time
Assume a list of tasks
  (A,C1, D1)(A,C2, D2) ...(A,Cn,Dn) that arrive at the same time i.e. A
How to find a feasible schedule?
  (there may be many feasible schedules)

## Slide 16: Earliest Due Date first (EDD) [Jackson 1955]
EDD: order tasks with non-decreasing deadlines.
  Simple form of EDF (earliest deadline first)
– Example: (1,10)(2,3)(3,5)
– Schedule: (2,3)(3,5)(1,10)
FACT: EDD is optimal
  If EDF cann’t find a feasible schedule for a task set, then no other algorithm can, i.e. The task set is non schedulable.

## Slide 17: Tasks with different arrival times
Assume a list of tasks
– S= (A1,C1, D1)(A2,C2, D2) ...(An,Cn,Dn)
Preemptive EDF [Horn 1974]:
  Whenever new tasks arrive, sort the ready queue according to earliest deadlines first at the moment
  Run the first task of the queue if it is non empty

## Slide 18: Earliest Deadline First Scheduling
Priorities are assigned according to deadlines:
  the earlier the deadline, the higher the priority;
  the later the deadline, the lower the priority

## Slide 19: EDF: Example

## Slide 20: Least slack scheduling
similar to shortest remaining time scheduling with the concept of a deadline thrown in.
pick the process that we can least afford to delay.
Least slack is computed as the time to the deadline minus the amount of computation.
For example, suppose that our remaining computation time, C, is 5 msec. and the deadline, D, is 20 msec from now. The slack time is D - C, or 15 msec.
The scheduler will compare this slack time with the slack times of other processes in the system and run the one with the lowest slack time.

## Slide 21: Least Slack Time scheduling
With earliest deadline, we will always work on the process with the nearest deadline, delaying all the other processes.
With least slack scheduling, we get a balanced result in that we attempt to keep the differences from deadlines balanced among processes.

## Slide 22: Processor Scheduling for Real-Time Rate Monotonic Scheduling (RMS)
Assume m periodic processes
  Process i requires ti msec of processing time every
pi msec.
  Equal processing every interval — like clockwork!

## Slide 23: Example
Periodic process i requires the CPU at specified intervals (periods)
pi is the duration of the period
ti is the processing time
di is the deadline by when the process must be serviced
– Often same as end of period

## Slide 24: Processor Scheduling for Real-Time
Rate Monotonic Scheduling (RMS)
Assume m periodic processes
  Process i requires ti msec of processing time every pi
msec.
  Equal processing every interval — like clockwork!
m
 1

i1
i
pi
t
Assume
Assign priority of process i to be
– Statically assigned
Let priority of non-real-time processes be 0
1
pi

## Slide 25: Rate Monotonic Scheduling (continued)
Scheduler simply runs highest priority process that is ready
  May pre-empt other real-time processes
  Real-time processes become ready in time for each frame or sound interval
  Non-real-time processes run only when no real- time process needs CPU

## Slide 26: Rate Monotonic Scheduling
priority is assigned based on the inverse of its period (its rate)"
  Shorter periods = higher priority;"
  Longer periods = lower priority“
P1 is assigned a higher priority than P2.

## Slide 27: Example
p1 = 50 msec; t1 = 20 msec
p2 = 100 msec; t2 = 35 msec
Priority(p1) > Priority(p2)
Total compute load is 75 msec per every 100 msec.
Both tasks complete within every period
  25 msec per 100 msec to spare

## Slide 28: Example 2
p1 = 50 msec; t1 = 25 msec
p2 = 80 msec; t2 = 35 msec
Priority(p1) > Priority(p2)
Total compute load is (25/50)+(35/80) = 0.94 = ~ 94% of CPU.
Cannot complete both tasks within some periods
  Even though there is still CPU capacity to spare!

## Slide 29: Processor Scheduling for Real-Time Earliest Deadline First (EDF)
When each process i become ready, it announces deadline Di for its next task.
Scheduler always assigns processor to process with earliest deadline.
  May pre-empt other real-time processes

## Slide 30: Earliest Deadline First Scheduling (continued)
No assumption of periodicity
No assumption of uniform processing times
Theorem: If any scheduling policy can satisfy QoS requirement for a sequence of real time tasks, then EDF can also satisfy it.
– Proof: If i scheduled before i+1, but Di+1 < Di , then i and i+1 can be interchanged without affecting QoS guarantee to either one.

## Slide 31: Earliest Deadline First Scheduling
EDF is more complex scheduling algorithm
  Priorities are dynamically calculated
  Processes must know deadlines for tasks
EDF can make higher use of processor than RMS
  Up to 100%
There is a large body of knowledge and theorems about EDF analysis

## Slide 32: Example 2 (again)
Priorities are assigned according to deadlines:
  the earlier the deadline, the higher the priority;
  the later the deadline, the lower the priority.
18/04/2018
44

## Slide 33
Thank You